## Slide 1: An Introductory Overview to SLAM Algorithms
Rishab Shah
April 30, 2017

## Slide 2: SLAM: Introduction
What is Simultaneous Localization and Mapping (SLAM)?
How do you solve the SLAM problem?

## Slide 3
Bachrach, Abraham, Ruijie He, and Nicholas Roy. “Autonomous Flight in Unknown Indoor Environments.” International Journal of Micro Air Vehicles 1 (2009): 217-228. DOI: 10.1260/175682909790291492

## Slide 4: Components of SLAM
Landmark Extraction
Data Association
State Estimation
State Update
Landmark Update
http://www.robotshop.com/media/files/images2/rplidar-360-laser-scanner-7-large.jpg

## Slide 5: State Estimation
Extended Kalman Filter
Bayesian Filter
Particle Filter
  Sequential Monte-Carlo Methods
  Rao- Blackwellized Particle Filter
Variants

## Slide 6: Extended Kalman Filter
Less computationally expensive for moderately dimensioned state space.
Convergence and consistency can be guaranteed in the linear model.
Robot Controls
Observations

## Slide 7: Extended Kalman Filter
Predict Step:
Update Step:
Map convergence is dependent on convergence of map covariance matrix and all landmark pair submatrices, towards zero, which in turn converge to a lower bound determined by initial uncertainties.

## Slide 8: Loop Closure
P. Newman and Kin Ho, "SLAM-Loop Closing with Visually Salient Features," Proceedings of the 2005 IEEE International Conference on Robotics and Automation, 2005, pp. 635-642.
Recognizing an already
mapped area.
Data Association with
high ambiguity.

## Slide 9: Loop Closure
P. Newman and Kin Ho, "SLAM-Loop Closing with Visually Salient Features," Proceedings of the 2005 IEEE International Conference on Robotics and Automation, 2005, pp. 635-642.
Uncertainties collapse
after a loop closure.

## Slide 10: Simulation

## Slide 11: Simulation

## Slide 12: Simulation

## Slide 13: Rao- Blackwellized Particle Filter
Particle Filters are non-parametric, recursive Bayes filters.
Not limited to Gaussian distributions and noise models.
Weighting at each step.
Resampling required.
Works well in low-dimensional spaces.
Monte-Carlo Localization, which is the standard for mobile robot localization today.

## Slide 14: Rao- Blackwellized Particle Filter
Joint SLAM state factored as robot component and conditional map component:
Directly represents non-linear process model.
Still linearizes the observation model but is a reasonable approximation for range-bearing measurements when robot pose is known.

## Slide 15: Rao- Blackwellized Particle Filter
Hugh Durrant-Whyte and Tim Bailey, Simultaneous Localisation and Mapping (SLAM): Part I The Essential Algorithms, IEEE Robotics and Automation Magazine, 2006, Vol.2

## Slide 16: Feature Extraction & Data Association
RANSAC (Random Sampling and Consensus) and variants (MSAC, MLSAC ,etc.) for feature extraction.
  Robust model fitting.
Data association use advanced image processing techniques that extract features from an image frame.
  HoG, LoG
  SIFT, SURF, BRIEF
  ORB, FREAK

## Slide 17: SIFT: Example
It may be very efficiently implemented and it is widely used for image matching in motion and object classification.

## Slide 18: History and State-of-the-art SLAM
Deterministic SLAM
2D SLAM
Online vs. Offline SLAM
Monocular vs. Stereo SLAM
Dense vs. Sparse Feature based SLAM
Discrete vs. Continuous-time SLAM
  Continuous-time uncertainty-constrained exploration, while maintaining localization uncertainty within given bounds.

## Slide 19: State-of-the-art SLAM algorithms
Raúl Mur-Artal and Juan D. Tardós. ORB-SLAM2: an Open-Source SLAM System for Monocular, Stereo and RGB-D Cameras. ArXiv preprint arXiv:1610.06475. 2016
An Introductory Overview to SLAM algorithms

## Slide 20: State-of-the-art SLAM algorithms
Vadim Indelman, Luca Carlone, Frank Dellaert , Planning in the continuous domain: A generalized belief space approach for autonomous navigation in unknown environments The International Journal of Robotics Research Vol 34, Issue 7, pp. 849 - 882
An Introductory Overview to SLAM algorithms

## Slide 21: Thank YOU